## Slide 1: An efficient heuristic for scheduling on parallel identical machines to minimize total tardiness
Benjamin Vincent
Nikolay Tchernev
Christophe Duhamel
Libo Ren
MIM 2016, 28-30 juin 2016, Troyes

## Slide 2
Process industries :
Production
line 1
Production
line n
Raw material
Products
Time
Demands :
Context
Notes: Industrie process où le pb de taille de lot ne se pose pas ( qui fabrique à la commande) != ordo cyclique

## Slide 3: Outline
Problem formulation
  Definition
  Formulation
  State of the art
Method
  Simulated Annealing based heuristic
  Dominance properties
  Pretreatment heuristic
  Building an initial solution
  Neighborhood definition
Results
Conclusion and further research

## Slide 4
Parallel machines :
Jobs have to be scheduled without pre-emption on one of the identical parallel machines. Each machine can process at most one job at a time. All the jobs and the machines are supposed to be available at time 0.
Problem formulation
Definition
Notes: Plein d’article sur machien paralleles : catégorie set up weithed ,,, ++artigues 2010

## Slide 5
Parallel machines :
Jobs have to be scheduled without pre-emption on one of the identical parallel machines. Each machine can process at most one job at a time. All the jobs and the machines are supposed to be available at time 0.
Problem formulation
Definition
Time
Demands :
machine 1
machine n
J1
J2
J3
J4
J5
J1
J2
J3
J4
J5
Jobs to be scheduled
Notes: Plein d’article sur machien paralleles : catégorie set up weithed ,,, ++artigues 2010

## Slide 6
n : number of jobs
m : number of machines
: tardiness of job i
: 1 if job i is scheduled before job j
: due date of job i
: completion time of job i
: processing time of job i
R : large enough
Problem formulation
Formulation

## Slide 7
Parallel machines problems:
Yin, Y., Cheng, S.R., Cheng, T.C.E., Wang, D.J., Wu, C.C. (2015). Just-in-time scheduling with two competing agents on unrelated parallel machines. Omega, 63, pp. 41–47.
Zinder, Y., Walker, S., (2015). Algorithms for scheduling with integer preemptions on parallel machines to minimize the maximum lateness, Discrete Applied Mathematics, 196, pp. 28–53.
Liu, Z., Lee, W.C., Wang, J.Y. (2016). Resource consumption minimization with a constraint of maximum tardiness on parallel machines. Computers & Industrial Engineering, 97,pp. 191–201.
Schwerdfeger, S., Walter, R. (2016) .A fast and effective subset sum based improvement procedure for workload balancing on identical parallel machines. Computers & Operations Research, 73, pp. 84–91.
Yin, Y., Cheng, T. C. E., Wang, D.J. (2016). Rescheduling on identical parallel machines with machine disruptions to minimize total completion time. European Journal of Operational Research, 252, pp. 737–749.
Problem formulation
States of the art
Notes: A, dominance+lb Y, ++dominance++lb T, relax + bb

## Slide 8
Non-exact methods for total tardiness minimization:
Biskup, D., Herrmann, J., & Gupta, J. N. (2008). Scheduling identical parallel machines to minimize total tardiness. International Journal of Production Economics, 115(1), pp. 134-142.
Demirel, T., Ozkir, V., Demirel, N. C., & Taşdelen, B. (2011). A genetic algorithm approach for minimizing total tardiness in parallel machine scheduling problems. In Proceedings of the World Congress on Engineering (2).
Exact methods:
Azizoglu, M., & Kirca, O. (1998). Tardiness minimization on parallel machines. International Journal of Production Economics, 55(2), pp. 163-168.
Yalaoui, F., & Chu, C. (2002). Parallel machine scheduling to minimize total tardiness. International Journal of Production Economics, 76(3), pp. 265-279.
Tanaka, S., and Araki, M. (2008). A branch-and-bound algorithm with Lagrangian relaxation to minimize total tardiness on identical parallel machines, International Journal of Production Economics, 113(1), pp. 446-458.
Problem formulation
States of the art
Notes: A, dominance+lb Y, ++dominance++lb T, relax + bb

## Slide 9
Method Simulated Annealing based heuristic
Notes: schémaaaaa

## Slide 10
Proposition 1: There exists an optimal schedule in which the sum of processing time of the jobs processed on each machine does not exceed the value given by the following equation:
Corollary 1: There exists an optimal schedule in which job j is processed at final position on any one of the machines if the following inequality holds:
Proposition 2: If all jobs have identical processing times then the Early Due Date (EDD) rule is optimal.
Proposition 3: If the process time exceeds due date for all jobs the Shortest Processing Time (SPT) rule is optimal.
Method
Dominance properties
Azizoglu et Kirca (1998)

## Slide 11
Initial data: list of jobs
Method Pretreatment heuristic
Processing Time | 8 | 6 | 9 | 4 | 7 | 5
Due date | 20 | 13 | 35 | 12 | 10 | 41
Corollary 1 criteria : 39
Processing Time | 8 | 6 | 9 | 4 | 7 | 5
Due date | 20 | 13 | 35 | 12 | 10 | 41
Reiterate on the remaining list of jobs : 34
Processing Time | 8 | 6 | 9 | 4 | 7
Due date | 20 | 13 | 35 | 12 | 10
Last iterate : 25

## Slide 12
Early Due Date:
Shortest Processing Time:
Minimum Slack Time: The schedule depends on the difference between the due date and the completion time.
Processing Time | 4 | 6 | 7 | 8
Due date | 12 | 13 | 10 | 20
Processing Time | 7 | 4 | 6 | 8
Due date | 10 | 12 | 13 | 20
Processing Time | 7 | 6 | 4 | 8
Due date | 10 | 13 | 12 | 20
10
12
9
Method Building an initial solution

## Slide 13
Switch two jobs:
Insert a job after an other:
Method Neighborhood
Insert a job on an empty machine:
Machine 1 | Job 4 | Job 8 | Job 7 | Job 5
Machine 2 | Job 6 | Job 2 | Job 1 | Job 3
Machine 1 | Job 4 | Job 1 | Job 7 | Job 5
Machine 2 | Job 6 | Job 2 | Job 8 | Job 3
Initial schedule:
Machine 1 | Job 4 | Job 7 | Job 5
Machine 2 | Job 6 | Job 2 | Job 1 | Job 8 | Job 3
Machine 1 | Job 4 | Job 8 | Job 7 | Job 5 | Job 6 | Job 2 | Job 3
Machine 2 | Job 1

## Slide 14
Probability to accept a solution j with a current solution i:
Method Temperature
Temperature update :
Kirkpatrick et al. (1983), Cerny (1995)
Ingber (1989)
Notes: schémaaaaa

## Slide 15
Dataset:
Results
Dataset
125 instances
m = 2 machines
n = 20 jobs
https://sites.google.com/site/shunjitanaka/pmtt
Yalaoui et Chu (2002): Branch and Bound, 25 groups of 5 instances
Tanaka and Araki (2008): Lagrangian relaxation + Branch and Bound

## Slide 16: Results
 | our heuristic |  | BAB YC1 |  | BAB YC2 | 
Instances | S | Temps | S | Temps | S | Temps
1 | 0% | 0,529 | 20% | 1518,2 | 20% | 1520,5
2 | 20% | 0,520 | 0% |  | 0% | 
3 | 100% | 0,523 | 20% | 1594,6 | 20% | 1594,6
4 | 100% | 0,519 | 40% | 1288,2 | 40% | 1324,2
5 | 100% | 0,527 | 80% | 1021,6 | 80% | 1049,5
6 | 20% | 0,524 | 0% |  | 0% | 
7 | 20% | 0,525 | 40% | 1447,8 | 40% | 1473,5
8 | 0% | 0,526 | 40% | 1082,8 | 40% | 1083,2
9 | 0% | 0,524 | 60% | 1109,0 | 60% | 1043,8
10 | 20% | 0,542 | 80% | 577,3 | 80% | 669,5
11 | 80% | 0,522 | 20% | 1470,3 | 20% | 1472,5
12 | 60% | 0,527 | 0% |  | 0% | 
13 | 60% | 0,520 | 0% |  | 0% | 
14 | 40% | 0,524 | 20% | 1538,3 | 20% | 1566,4
15 | 40% | 0,527 | 60% | 1259,9 | 40% | 1390,2
16 | 80% | 0,534 | 100% | 762,5 | 100% | 782,1
17 | 100% | 0,536 | 60% | 924,3 | 60% | 982,2
18 | 100% | 0,523 | 40% | 1083,1 | 40% | 1083,3
19 | 60% | 0,539 | 20% | 1564,3 | 20% | 1632,0
20 | 60% | 0,527 | 80% | 1482,2 | 80% | 1259,9
21 | 100% | 0,531 | 100% | 0,6 | 100% | 0,7
22 | 100% | 0,521 | 100% | 42,1 | 100% | 56,9
23 | 100% | 0,529 | 100% | 748,2 | 100% | 855,3
24 | 100% | 0,530 | 60% | 775,3 | 60% | 790,5
25 | 100% | 0,529 | 60% | 1027,3 | 60% | 1119,6
Average | 62% | 0,527 | 48% | 1062,7 | 47% | 1083,4
Yalaoui and Chu (2002)
6% from the optimality on average for the unsolved instances (47/125)
16 optima found on 17 for the no-late instances
Notes: +5 BAB %%%%%%

## Slide 17: Results
 | Our heuristic | Tanaka and Araki
Av. Time | 0,527 | 0.656
Max. Time | 0,557 | 2.282
Solutions at Less than 1% from optimum | 84/125 | 105/125
Tanaka and Araki (2008)
Comparison with the Lagrangian relaxation:

## Slide 18
Conclusion and further research
Conclusion:
  An efficient heuristic for scheduling on parallel identical machines
Further research:
  Test on larger datasets
  Build a Branch and Bound method

## Slide 19
Thanks for your attention

## Slide 20: Branch and Bound
Temps | 4 | 5 | 7 | 8
Echéance | 15 | 13 | 10 | 20
Temps | 4 | 5 | 7 | 8
Echéance | 10 | 13 | 15 | 20
LB =5
UB =10
LB =8
LB =10
14
LB=18

## Slide 21
Problem formulation
States of the art
Resource consumption minimization
Workload balancing
Total completion time minimization
Total tardiness and earliness minimization
Maximum lateness
Y. Zinder and
S. Walker (2015)
Y. Yin et al. (2015)
S. Schwerdfeger and
R. Walter (2016)
Z. Liu et al. (2016)
Y. Yin et al. (2016)
Parallel machines problems :
Notes: A, dominance+lb Y, ++dominance++lb T, relax + bb

## Slide 22
Non-exact methods :
Demirel, T., Ozkir, V., Demirel, N. C., & Taşdelen, B. (2011). A genetic algorithm approach for minimizing total tardiness in parallel machine scheduling problems. In Proceedings of the World Congress on Engineering (2).
Andres, F., Lara, B., Yalaoui, F., & Dugardin, F. (2012). A Tabu Search Algorithm to Minimize the Total Tardiness in the Parallel Machines Scheduling Problem. 14th IFAC Symposium on Information Control Problems in Manufacturing, pp. 1371-1376.
Exact methods:
Azizoglu, M., & Kirca, O. (1998). Tardiness minimization on parallel machines. International Journal of Production Economics, 55(2), pp. 163-168.
Yalaoui, F., & Chu, C. (2002). Parallel machine scheduling to minimize total tardiness. International Journal of Production Economics, 76(3), pp. 265-279.
Tanaka, S., and Araki, M. (2008). A branch-and-bound algorithm with Lagrangian relaxation to minimize total tardiness on identical parallel machines, International Journal of Production Economics, 113(1), pp. 446-458.
Problem formulation
States of the art
Notes: A, dominance+lb Y, ++dominance++lb T, relax + bb